## Slide 1: Challenge 8
Team members:
Shisheng wang
xiangtian yi
Ye xing
Yanlin zhou

## Slide 2
 | Xiangtian | Shisheng | Ye | Yanlin
Challenge 1 | Presenter |  |  | 
Challenge 2 |  | Presenter |  | 
Challenge 3 |  |  | Presenter | 
Challenge 4 |  |  |  | Presenter
Challenge 5 |  |  | Presenter | 
Challenge 6 |  | Presenter |  | 
Challenge 7 |  |  |  | Presenter
Challenge 8 | Presenter |  |  | 
Presenter on this challenge

## Slide 3
Xiangtian | Shisheng | Ye | Yanlin
I set up the camera, fixed the patch bug within it. Helped designing the UI. Besides, I implemented the first part of the node.js file for remotely controlling the car. | I set up 4 beacons and recorded the localization data,I tested lots of data to make it accurate to show the location on the webpage. | I mainly designed the code of arduino for auto and manual driving. Testing the car with Yanlin and implemented the localization code. | Designed the UI and programmed the webpage. Integrated the car. Optimized the PID control and designed the passing-gap algorithm with Ye Xing. Testing the car.
TEAM WORK

## Slide 4: architecture
Beacon 1
Beacon 2
Beacon 3
Beacon 4
RSSI
RSSI
RSSI
RSSI
Coordinator
Node.js
Coordinator
router

## Slide 5: Photos of developed system

## Slide 6: DESIGN DECISIONS
Sensors
  2 LIDAR sensor on both sides
    Using the smaller value to control the car
    Accurate measures
  1 Ultrasonic sensor in the front
    Effectively detecting things ahead
    scalable

## Slide 7
DESIGN DECISION
Algorithm choose
  Compared with other methods, KNN is a better solution for Xbee
  Implement it on Raspberry Pi
  Use Node.js KNN library to train the dataset and define the location
Front end
  Design a map on webpage and use a point to show the location
Jumpy data correction
  Use queue to store data and take the average to predict
  Record the previous location data and we set a bound to limit the difference between previous and current lower than 1 step.

## Slide 8: DESIGN DECISIONS
Control Algorithms
  Side
    PID: Distance to both sides of wall
    Adapt the output to adjust the wheel direction
    Bound control
  Front
    Read data from the ultrasonic sensor and stop if obstacle ahead
  Remote Control
    Use Xbee to remote start and stop the car

## Slide 9: Challenge & future improvement
Challenges:
  Test the PID control and Re-adjust the most suitable parameter
  The localization is not accurate because of the weak wifi signal
  Test multiple ways to pass the elevator hall
  Manual control latency because of the weak signal
  Patch setting of the camera
Improvement:
  Turning accuracy
  Localization accuracy
  Turning speed
  Manual control speed

## Slide 10
Thank you !